## Slide 1: VSD 2020 Project Presentation Correlation Filter – based Object Tracking System
Team : VLSILAB
Members : 陳韋呈 黃建智 邱建智 黑崇瑜 高士鈞

## Slide 2: Member Introduction
陳韋呈
黃建智
邱建智
黑崇瑜
高士鈞

## Slide 3: Outline
Introduction to the Application
Algorithm Analysis
System Architecture and Operating Flow
AP Architecture
System Specification
Benchmark
Conclusion and Future Work

## Slide 4: Introduction to the Application
Correlation Filter : An online-training correlation filter
  Introduce the concept of signal correlation (Convolution) in DSP, DCF is a filter to calculate the correlation between filter and input frame.
  To reduce the computing complexity, the correlation computing and the filter updating are both processed in frequency domain by doing Fast Fourier Transform.
D. S. Bolme, J. R. Beveridge, B. A. Draper and Y. M. Lui, "Visual object tracking using adaptive correlation filters", 2010 CVPR.

## Slide 5: Correlation Filter – Tracking Process
Updating:
  Update the filter according to the given input feature of the tracking target.
Tracking :
  After filter updating, the location corresponding to the maximum value in the correlation output indicates the new position of the target.
  The filter updating is then performed based on that new location.
Updating the Filter
Tracking the Object
Input
Filter
Response

## Slide 7: Algorithm
Input Image :
Correlation Filter :
Correlation :
Desired Output :
  = 2D Gaussian shaped peak ()
MOSSE finds a filter H that minimizes the sum of squared error between the actual output of the convolution and the desired output of the convolution.
Minimization Problem :
Lower case : spatial domain
Upper case : frequency domain
: FFT
: Element-wise multiplication
, i : i-th frame
Notes: Desired Output (也就是Ground Truth)是一個很強的response並且集中座落在search window的中心
作者使用2D的高斯分布當作訓練的ground truth
MOSSE的cost function是定義實際output和gt差值平方的累積總和
也就是說前幾個frame的資訊會一直被累積，且影響當前filter的更新

## Slide 8: Derivation
Notes: 要解這個最佳化問題，很直觀的就是對cost function做對H bar的偏微分

## Slide 9: Algorithm Analysis
Dominant Function:
  Spatial – Frequency Transformation
  Simplified Filter Calculation :
AP Specific Operation :
  2D Fast Fourier Transformation (FFT)
  2D Inverse Fast Fourier Transformation (IFFT)
  Complex Number Multiplication
  Complex Number Division

## Slide 10: System Architecture
AXI
L1C_Cache
L1D_Cache

## Slide 11: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
L1C_Cache
L1D_Cache

## Slide 12: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
2. CPU send Control Signal to AP
(FFT + Divide)
L1C_Cache
L1D_Cache

## Slide 13: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
2. CPU send Control Signal to AP
(FFT + Divide)
3. When AP operating, CPU move data from DRAM to AP (Frame1)
L1C_Cache
L1D_Cache

## Slide 14: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
2. CPU send Control Signal to AP
(FFT + Divide)
3. When AP operating, CPU move data from DRAM to AP (Frame1)
4. CPU send Control Signal to AP
(FFT + Multiply + IFFT)
L1C_Cache
L1D_Cache

## Slide 15: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
2. CPU send Control Signal to AP
(FFT + Divide)
3. When AP operating, CPU move data from DRAM to AP (Frame1)
4. CPU send Control Signal to AP
(FFT + Multiply + IFFT)
5. CPU wait for AP by accessing the specific location of AP.
L1C_Cache
L1D_Cache

## Slide 16: Operating Flow
1. CPU move data from DRAM to AP (Frame0)
2. CPU send Control Signal to AP
(FFT + Divide)
3. When AP operating, CPU move data from DRAM to AP (Frame1)
4. CPU send Control Signal to AP
(FFT + Multiply + IFFT)
5. CPU wait for AP by accessing the specific location of AP.
6. CPU load the response map from AP and find the location of max value.
7. Repeat 1~6
L1C_Cache
L1D_Cache

## Slide 17: AP Architecture
Slave
Register
Frame
(4KB)
Slave
Register
Response
(4KB)
1024-Point
2D FFT
32-bit
Complex
Number
Divider
Filter
Params
Memory
(8KB)
32-bit
Complex
Number
Multiplier
1024-Point
2D IFFT
Controller
Input Frame
Control Signal
Output Response
AXI

## Slide 18: 2D FFT
Flow :
  1. Do 32-point FFT to each row
  2. Do 32-point FFT to each column
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
 |  | … |  | 
… | … |  | … | …
 |  | … |  | 
 |  | … |  | 

## Slide 19: 1024-Point 2D FFT/IFFT
Real_out
Imag_out
32-point
FFT/IFFT
Local MEM
Local MEM
Real_in
Imag_in
Re-index
Folding Architecture

## Slide 20: 32-point FFT
R2SDF
  Radix-2 Single-Path Delay Feedback
  5 Butterfly Units, 3 Complex Multipliers
Data : 32-bit Fixed-Point Value
Twiddle Factor : 16-bit Fixed-Point Value

## Slide 21: 32-bit Divider
  32-stage pipeline divider.
  Use subtraction to realize divide operation.
A[31:0]
B[31:0]
Divide
Unit
30’d0,A[31]
C[31]
D0[31:0]
Pipeline Stage 0
Divide
Unit
B[31:0]
D0[30:0],
A[30]
D1[31:0]
C[30]
A[30:0]
B[31:0]
Pipeline Stage 1
……
Pipeline Stage 31
C[31:0]
C[31]
a[31:0]
b[31:0]
A>B?
1
0
c
A-B
d[31:0]
D[31:0]

## Slide 22: System Specification
 | Synthesis | APR
Max working frequency | 80 MHz | 
Power | 206.72 mW | 874.65 mW
Area | 12,618,973 | 10,283,874
Processing Speed | Only AP | AP + CPU
 | 10,000 FPS | 25 FPS
Data bit width | 32-bit Fixed-Point Value (Q15.16) | 
 | Synthesis | APR
Max working frequency | 80 MHz | 
Power | 206.72 mW | 874.65 mW
Area |  | 
Processing Speed | Only AP | AP + CPU
 | 10,000 FPS | 25 FPS
Data bit width | 32-bit Fixed-Point Value (Q15.16) | 

## Slide 23: Benchmark
We prepare ten sets of 3-frame video sequences.
  To compute the bounding box’s IOU between our result and the groundtruth.
  Average IOU : 85%
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
frame1 | 100% | 90.8% | 35.2% | 100% | 100% | 96.9% | 100% | 100% | 93.8% | 29.7%
frame2 | 100% | 93.8% | 23.4% | 96.9% | 100% | 96.9% | 100% | 100% | 90.8% | 42.5%
*Groundtruth of frame0 is given for the main program to initialize the filter.
Red : Groundtruth / Blue : Inference

## Slide 24: Conclusion and Future Work
Conclusion
  Our AP can operate 1024-point 2D FFT/IFFT ,32-bit complex number division and multiplication. And can be used to accelerate the correlation-based object tracking algorithm.
  The system can work at 80 MHz, and speed up to 25 FPS.
Future Work
  The system spends too much time on data movement.
    Direct Memory Access
    AXI Burst Mode
  Because the lack of DMA, CPU always needs to move the data from DRAM to AP. If DMA is available, parallel processing can be realized.
    Ex: When AP is doing FFT + divide (Filter Update), CPU can do FFT for response calculation.